## Slide 1: Real Time Data Exchange (RDTE) Toolbox

## Slide 2: Summary
Provides a scripting interface to allow for easier manipulation of the UR5e
Sends Urscript commands as byte strings to the UR5e
Can send:
  Movej
  Movel
  Movec
  Movep
  Paths!
Can receive:
  Pose/Joint position
  Joint Velocity
  Joint Acceleration
  Joint Torque

## Slide 3: Setup
VM Installation
  VmWare : Almost everyone
  VirtualBox : If for some reason vmware doesn’t work
Setup port forwarding (Only required for Virtualbox. If you are using VMware don't worry about this)
Setup RTDE folder path in MATLAB
If you use virtualbox, your screen may flicker. This issue is not present with vmware.

## Slide 4: Laptop Side setup: Everyone
Connect ur5e ethernet cable to laptop or pc (Orange cable)
Go to ethernet settings
Change to manual
Turn on IPv4
Set IP address to “192.168.0.77”
Set subnet mask to “255.255.255.0”

## Slide 5: For operation
Make sure that the UR5e is In remote control mode.
  Switch to automatic then to remote control mode
This is only required on the actual UR5e. Not needed on the VM

## Slide 6: TCP Connection Setup
Only once in the program
Port = 30003
When connecting to the VM: (select only the IP address that aligns with the application that you are using)
  Host = 127.0.0.1 (Virtualbox)
  Host = ‘192.168.230.128’ (Vmware)
When connecting to the UR5e:
  Host = 192.168.0.100
Finally call the constructor:
  rtde = rtde(host,port)
Host on the UR5e must be configured correctly for this to work. The demonstrators will have already set this up.
You can also use your own laptop by connecting the ethernet port directly to your laptop. You will also need to configure the ethernet connection on your PC for it to work.

## Slide 7: Functions

## Slide 8: movej : Move to position (linear in joint space)
When using this command, the robot must be at a standstill or come from a movej or movel with a blend. The speed and acceleration parameters control the trapezoid speed profile of the move. Alternatively, the t parameter can be used to set the time for this move. Time setting has priority over speed and acceleration settings
Definition:
[poses,joints,jointVelocities,jointAccelerations,torques] = movej(target,jointOrPose,a,v,t,r)

## Slide 9: movej : Move to position (linear in joint space)
[poses,joints,jointVelocities,jointAccelerations,torques] = movej(target,jointOrPose,a,v,t,r)
PARAMETERS:
Target = Joint position or pose.
jointOrPose = "joint" or "pose" to provide joint inputs or pose inputs
a = joint acceleration (rad/s^2) (default = 1.4)
v = joint speed (rad/s) (default = 1.05)
t = time (s) (default = 0). If specified it will ignore the a and v values
r = blend radius (of target pose) (m) (default = 0)

## Slide 10: movej : example usage
target = [-588.53, -300, 200, 2.2214, -2.2214, 0.00];
 | command
Output pose and input xyzrpy | pose = rtde.movej(target)
Output pose and joint position and input xyzrpy | [pose,jointPos] = rtde.movej(target)
Output pose, joint position, joint velocity | [pose,jointPos,jointVel] = rtde.movej(target)
Output pose, joint position, joint velocity, joint acceleration | [pose,jointPos,jointVel, jointAcc] = rtde.movej(target)
Output pose, joint position, joint velocity, joint acceleration, joint torque | [pose,jointPos,jointVel, jointAcc, jointTor] = rtde.movej(target)
Only want joint position | [~,jointPos] = rtde.movej(target)
Only want joint velocity | [~,jointPos,~] = rtde.movej(target)
Want joint position and joint acceleration | [~,jointPos,~, jointAcc] = rtde.movej(target)

## Slide 11: movej : example usage
target = [-2.4670 -2.1287 -1.6192 -0.9645 1.5708 -2.4670];
 | command
Output pose and input joint position | pose = rtde.movej(target,’joint’)
Output pose, joint position, joint velocity, joint acceleration, joint torque and input joint positions | [pose,jointPos,jointVel, jointAcc, jointTor] = rtde.movej(target,’joint’)
Want joint position and joint acceleration and input ‘joint’ positions | [~,jointPos,~, jointAcc] = rtde.movej(target,’joint’)
If you want to set acceleration, velocity or blend radius input variables. a = tool acceleration v = tool speed r = blend radius You will still need to provide a value t = 0. Remember if t > 0 it will override a and v | [pose] = rtde.movej(target,’joint’,a,v,t,r) If via_point and target positions are a pose, you need to use: [pose] = rtde.movej(target,’pose’,a,v,t,r)
If you want to set a value for time: e.g. t = 5 Again you will still need to input a and v, but they can be set to 0. | [pose] = rtde.movej(target,’joint’,a,v,t,r) If via_point and target positions are a pose, you need to use: [pose] = rtde.movej(target,’pose’,a,v,t,r)

## Slide 12: movel : Move to position (linear in tool space)
[poses,joints,jointVelocities,jointAccelerations,torques] = movel(target,jointOrPose,a,v,t,r)
PARAMETERS:
Target = Joint position or pose.
jointOrPose = "joint" or "pose" to provide joint inputs or pose inputs
a = joint acceleration (m/s^2) (default = 1.4)
v = joint speed (m/s) (default = 1.05)
t = time (s) (default = 0). If specified it will ignore the a and v values
r = blend radius (of target pose) (m) (default = 0)

## Slide 13: movel : example usage
target = [-588.53, -300, 200, 2.2214, -2.2214, 0.00];
 | command
Output pose and input xyzrpy | pose = rtde.movel(target)
Output pose and joint position and input xyzrpy | [pose,jointPos] = rtde.movel(target)
Output pose, joint position, joint velocity | [pose,jointPos,jointVel] = rtde.movel(target)
Output pose, joint position, joint velocity, joint acceleration | [pose,jointPos,jointVel, jointAcc] = rtde.movel(target)
Output pose, joint position, joint velocity, joint acceleration, joint torque | [pose,jointPos,jointVel, jointAcc, jointTor] = rtde.movel(target)
Only want joint position | [~,jointPos] = rtde.movel(target)
Only want joint velocity | [~,jointPos,~] = rtde.movel(target)
Want joint position and joint acceleration | [~,jointPos,~, jointAcc] = rtde.movel(target)

## Slide 14: movel : example usage
target = [-2.4670 -2.1287 -1.6192 -0.9645 1.5708 -2.4670];
 | command
Output pose and input joint position | pose = rtde.movel(target,’joint’)
Output pose, joint position, joint velocity, joint acceleration, joint torque and input joint positions | [pose,jointPos,jointVel, jointAcc, jointTor] = rtde.movel(target,’joint’)
Want joint position and joint acceleration and input ‘joint’ positions | [~,jointPos,~, jointAcc] = rtde.movel(target,’joint’)
If you want to set acceleration, velocity or blend radius input variables. a = tool acceleration v = tool speed r = blend radius You will still need to provide a value t = 0. Remember if t > 0 it will override a and v | [pose] = rtde.movel(target,’joint’,a,v,t,r) If via_point and target positions are a pose, you need to use: [pose] = rtde.movel(target,’pose’,a,v,t,r)
If you want to set a value for time: e.g. t = 5 Again you will still need to input a and v, but they can be set to 0. | [pose] = rtde.movel(target,’joint’,a,v,t,r) If via_point and target positions are a pose, you need to use: [pose] = rtde.movel(target,’pose’,a,v,t,r)

## Slide 15: movep : Blend circular and move linear (in tool space)
Definition: [poses,joints,jointVelocities,jointAccelerations,torques] = movep(obj,target,jointOrPose,a,v,r)
Example use case is exactly the same as movej and movel. Please refer to those.
Due to the safety limits on the UR5e, it might not work as it tends to try to go at a velocity about the limit. But try it out and see what happens!

## Slide 16: movec : Circular Move: Move to position (circular in tool-space)
TCP moves on the circular arc segment from current pose, through pose_via to pose_to. Accelerates to and moves with constant tool speed v. Use the mode parameter to define the orientation interpolation.
Definition:
[poses,joints,jointVelocities,jointAccelerations,torques] = movec(via_point,pose_to,jointOrPose,a,v,r,mode)

## Slide 17: movec : Circular Move: Move to position (circular in tool-space)
[poses,joints,jointVelocities,jointAccelerations,torques] = movec(via_point,pose_to,jointOrPose,a,v,r,mode)
PARAMETERS:
pose_via = path point Pose_via, can also be specified as joint positions, then forward kinematics is used to calculate the corresponding pose.
pose_to = arget pose Pose_to can also be specified as joint positions, then forward kinematics is used to calculate the corresponding pose.
jointOrPose= "joint" or "pose" to provide joint inputs or pose inputs
a = tool acceleration (m/s^2) (default = 1.2)
v = tool speed (m/s) (default = 0.25)
r = blend radius (of target pose) (m) (default = 0.05)
mode = 0: Unconstrained mode. Interpolate orientation from current pose to target pose (pose_to)
mode = 1: Fixed mode. Keep orientation constant relative to the tangent of the circular arc(starting from current pose)
(mode default = 1)

## Slide 18: movec : example usage
via_point = [-588.53, -300, 400, 2.2214, -2.2214, 0.00];
target = [-588.53, -300, 200, 2.2214, -2.2214, 0.00];
 | command
Output pose and input xyzrpy | pose = rtde.movec(via_point,target)
Output pose and joint position and input xyzrpy | [pose,jointPos] = rtde.movec(via_point,target)
Output pose, joint position, joint velocity | [pose,jointPos,jointVel] = rtde.movec(via_point,target)
Output pose, joint position, joint velocity, joint acceleration | [pose,jointPos,jointVel, jointAcc] = rtde.movec(via_point,target)
Output pose, joint position, joint velocity, joint acceleration, joint torque | [pose,jointPos,jointVel, jointAcc, jointTor] = rtde.movec(via_point,target)
Only want joint position | [~,jointPos] = rtde.movec(via_point,target)
Only want joint velocity | [~,jointPos,~] = rtde.movec(via_point,target)
Want joint position and joint acceleration | [~,jointPos,~, jointAcc] = rtde.movec(via_point,target)

## Slide 19: movec : example usage
via_point = [-588.53, -300, 400, 2.2214, -2.2214, 0.00];
target = [-588.53, -300, 200, 2.2214, -2.2214, 0.00];
x,y,z are in mm and r,p,y are in radians
 | command
Output pose and input joint position | pose = rtde.movec(via_point,target)
Output pose and joint position and input xyzrpy | [pose,jointPos] = rtde.movec(via_point,target)
Output pose, joint position, joint velocity | [pose,jointPos,jointVel] = rtde.movec(via_point,target)
Output pose, joint position, joint velocity, joint acceleration | [pose,jointPos,jointVel, jointAcc] = rtde.movec(via_point,target)
Output pose, joint position, joint velocity, joint acceleration, joint torque | [pose,jointPos,jointVel, jointAcc, jointTor] = rtde.movec(via_point,target)
Only want joint position | [~,jointPos] = rtde.movec(via_point,target)
Only want joint velocity | [~,jointPos,~] = rtde.movec(via_point,target)
Want joint position and joint acceleration | [~,jointPos,~, jointAcc] = rtde.movec(via_point,target)

## Slide 20: movec : example usage
via_point = [-2.4670 -1.9549 -1.3324 -1.4250 1.5708 -2.4670];
target = [-2.4670 -2.1287 -1.6192 -0.9645 1.5708 -2.4670];
 | command
Output pose and input joint position | pose = rtde.movec(via_point,target,’joint’)
Output pose, joint position, joint velocity, joint acceleration, joint torque and input joint positions | [pose,jointPos,jointVel, jointAcc, jointTor] = rtde.movec(via_point,target,’joint’)
Want joint position and joint acceleration and input ‘joint’ positions | [~,jointPos,~, jointAcc] = rtde.movec(via_point,target,’joint’)
If you want to set acceleration, velocity or blend radius input variables. a = tool acceleration v = tool speed r = blend radius | [pose] = rtde.movec(via_point,target,’joint’,a,v,r) If via_point and target positions are a pose, you need to use: [pose] = rtde.movec(via_point,target,’pose’,a,v,r)

## Slide 21: Other functions
Get actual tool pose (x,y,z,r,p,y) (m and radians) | pose = rtde.actualPosePositions()
Get target tool pose | pose = rtde.targetPosePositions()
Get actual joint position | jointPos = rtde.actualJointPositions()
Get target joint positions | jointPos = rtde.targetJointPositions()
Plot tool path (poses) | rtde.drawPath(listOfPoses)
Plot joint positions | rtde.drawJointPositions(listOfJointPositions)
Plot joint velocities | rtde.drawJointVelocities(listOfJointVelocities)
Plot joint accelerations | rtde.drawJointAccelerations(listOfJointAccelerations)
Plot joint torques | rtde. drawJointTorques(listOfTorques)

## Slide 22: Robot Mode
mode = rtde.checkRobotMode()
% RETURN VALUES:
%-1 : ROBOT_MODE_NO_CONTROLLE
% 0 : ROBOT_MODE_DISCONNECTED
% 1 : ROBOT_MODE_CONFIRM_SAFETY
% 2 : ROBOT_MODE_BOOTING
% 3 : ROBOT_MODE_POWER_OF
% 4 : ROBOT_MODE_POWER_ON
% 5 : ROBOT_MODE_IDLE
% 6 : ROBOT_MODE_BACKDRIVE
% 7 : ROBOT_MODE_RUNNING
% 8 : ROBOT_MODE_UPDATING_FIRMWARE

## Slide 23: Safety mode
safety = rtde.checkSafetyMode()
% RETURN VALUES:
% 1 : SAFETY_MODE_NORMAL
% 2 : SAFETY_MODE_REDUCED
% 3 : SAFETY_MODE_PROTECTIVE_STOP
% 4 : SAFETY_MODE_RECOVERY
% 5 : SAFETY_MODE_SAFEGUARD_STOP
% 6 : SAFETY_MODE_SYSTEM_EMERGENCY_STOP
% 7 : SAFETY_MODE_ROBOT_EMERGENCY_STOP
% 8 : SAFETY_MODE_VIOLATION
% 9 : SAFETY_MODE_FAULT
% 10 : SAFETY_MODE_VALIDATE_JOINT_ID
% 11 : SAFETY_MODE_UNDEFINED_SAFETY_MODE

## Slide 24: Debugging
If you get an error saying “Unrecognised function or variable ‘rtde’”, that means you have not correctly set the path to the location of the rtde folder in matlab.
  Please follow instructions here: https://github.com/rag-h/mtrn4230_course_development